## Slide 1: First light of 東北大 Haleakala 60cm 望遠鏡 (T60) in Sep. 2014: 超高波長分解能レーザヘテロダイン分光器の 惑星への挑戦
中川広務1, 青木翔平1,2, 笠羽康正1, 村田功1
Guido Sonnabend4, 佐川英夫3, 岡野章一1,5, 鍵谷将人1
*坂野井健1, Jeff Kuhn5, Joe Ritter5, 伊藤一成1
（1東北大, 2IAPS/INAF (Italy), 3京都産業大,
4Radiometer Physics GmbH (Germany), 5Univ. Hawaii）
2014年12月4日第４回可視赤外線観測装置技術ワークショップ（三鷹）

## Slide 2: なぜ惑星大気観測のために赤外高分散分光が 必要なのか？
- ダイナミクス、化学反応のトレーサーとなり得る微量気体や同位体比（火星メタン、H2O/HDO等）の測定
- 惑星高層希薄大気中のnon-LTE発光の測定
- 詳細スペクトルから気体数密度（高度プロファイルも）や、ドップラーシフトから風速を測定
- 地球大気と惑星大気の吸収線または発光線の分離

## Slide 3
T60 Open Ceremony - 8 Sep. 2014

## Slide 4: Night View of Tohoku Univ. 60cm (T60)
晴天率0.6～0.7

## Slide 5: Purpose of Tohoku Univ. 60cm (T60)
Flexible - Conjugated operations with large telescopes & space missions
Continuous monitoring - Temporal variabilities in diurnal, seasonal solar cycle
Unique instrument – including ‘Infrared’ and visible high-resolution spectroscopy
[First instrument]
Mid-Infrared LAser Heterodyne Instrument (MILAHI) λ/dλ ~ 106-7
Visible filter imager
[Future plan]
Visible Echelle spectrometer λ/dλ ~ 50000
Near-Infrared (1-5um) Echelle spectrometer (ESPRIT) λ/dλ ~ 20000

## Slide 6
IR Heterodyne instrument on T60 (Sep. 2014) [Credit: Ohkusa]

## Slide 7: IR heterodyne: Principle
Ihet = RTOA RLO
RTOA = εB(Tsurf) e-τ + RUW
Ihet = IDC + IIF = PS + PL + 2√ PSPLcos(2π γIF t - φ)
IR flux from the planet through its atmosphere ...
… is combined with IR from local (laser) and
focused on Photomixer.
Output is in Radio region (Bandwidth: ~2 GHz) of the electromagnetic spectrum.
PHOTOMIXER
MCT detector
Bandwidth 2GH
ZNSE
BEAM SPLITTER
QC LASER
FLIP MIRROR
CALIBRATOR
TELESCOPE

## Slide 8: Advantage of IR heterodyne
Sensitive detection of minor trace gases
Wind and temperature (10 m/s & 10K accuracy)
Mapping with vertical profiles (3D structure)
Many organic molecules
Small-sized (good for space-, balloon- applications)

## Slide 9
O3
O3(668)
O3(668)
O3(667)
Observed terrestrial O3 at Laboratory in coelostat sunlight at 1043.864 cm-1 (1GHz bandwidth, 1MHz res., 10min integration time on Mar. 2014)
IR heterodyne
Calculation
Data at Laboratory with Sun light (ATRC, Univ. Hawaii)

## Slide 10
Reduced sunlight is led into the instrument.
Sun (terrestrial atmosphere) at T60 !

## Slide 11
Observed terrestrial CO2 spectrum with T60 at 970.532 cm-1
(1GHz bandwidth, 2MHz res., 5min integration time on 3 Sep. 2014)
0.02cm-1
IR heterodyne
Calculation
Sun (terrestrial atmosphere) at T60 !

## Slide 12
Observed Martian CO2 spectrum by T60 at 970.532 cm-1 (2MHz res.)
on 14 Nov. 2014
(ref) Previous study
[Sonnabend et al., 2006].
First detection of Mars non-LTE emission with T60 !
Fig. Mars CO2 non-LTE emission spectrum obtained by IR heterodyne instrument onboard T60 on 11 November 2014. Integration time is 10min. FOV is located at the center of Martian disk.

## Slide 13
Heterodyne Target: with λ/dλ>1,500,000
Isotope map, HDO/H2O
(Villanueva+, 2008)
Seasonal var. of oxidisor, H2O2
(Lefevre+, 2009)
IRTF/HIPWAC
(Fast+, 2009)
Mesospheric Wind and T
(Nakagawa+, 2013)
Detection of CH4
(Sonnabend+, 2009)

## Slide 14
64”
15”
3.5”@10um
Mars
Venus
Beam
size
2.6”@7um
Fig. Comparison between the instrumental FOV of Tohoku 60cm-telescope and targets. Resolved disk image can be obtained to investigate global distributions of physical parameters.
Spatial Resolution of MILAHI with T60

## Slide 15
UVIS (0.20 – 0.65 mm) l/Dl ~ 250
IR (2.3 – 3.8 mm) l/Dl ~ 10,000
IR (2.3 – 4.3 mm) l/Dl ~ 20,000
ACS
Suite of 3 high-resolution
spectrometers
Near IR (0.7 – 1.7 mm) l/Dl ~ 20,000
Atmospheric chemistry, aerosols, surface T,
structure
IR (Fourier, 2 – 25 mm) l/Dl ~ 4000 (SO)/500 (N)
Mid IR (2.2 – 4.5 mm) l/Dl ~ 50,000
Nadir
Limb
SO
Nadir
CaSSIS
High-resolution camera
Mapping of sources;
landing site selection
FREND
Collimated neutron detector
Mapping of
subsurface water
NOMAD
High resolution occultation
and nadir spectrometers
Atmospheric composition
(CH4 ,O3 , trace species, isotopes)
dust, clouds, P&T profiles
ESA + Roscosmos
SO
SO
Nadir
SO
Limb
SO
2016 Launch
Trace Gas Orbiter
MAVEN
NASA
2015-

## Slide 16
Haleakala 2m telescope ‘PLANETS’ meeting (Sep. 7, 2014)
First light: end of 2016 [fastest case]
Gregorian focus
F/12.8 (f=23040mm)
Coude
(F/50)

## Slide 17: Summary
MILAHI, a new infrared heterodyne instrument with λ/dλ ~ 106-7 finally started its initial run attached to Haleakala T60.
Feasibility on T60 was demonstrated by solar observations (terrestrial and solar atmospheres).
We are going to Martian observations in Nov 2014 and March-September 2015 for the monitor of lower atmosphere just below MAVEN observations.